10.03.2022
Beta version of software for intercom consoles (PDO), stage 1+, patch 4
The threshold of detector for the microphone in the sound loop effect suppression module has been adjusted based on the results of a study of the microphone path characteristics of the consoles on various speech fragments.

21.02.2022
Beta version of software for intercom consoles (PDO), stage 1+, patch 4
1. updated missed call indication (according Technical Requiriments)
2. increased sound muting level for sound ring effect suppression algorithm, due to differences in the parameters of microphone analog path by default
28.01.2022

Beta version of software for intercom consoles (PDO), stage 1+, patch 3
1. added module with algorithm for sound ring effect suppression (moved from audiocodec driver)
2. updated algorithm for sound ring effect suppression (fine tuning to work at minimum and maximum microphone sensivity levels)
3. updated audiocodec driver (volume and sensitivity ranges)
4. updated doxygen documentation

24.01.2022
Beta version of software for intercom consoles (PDO), stage 1+, patch 2
1. updated algorithm for ring effect suppression (algorithm settings fine setup)
2. added automatic disabling ring effect suppression algoritm in simplex mode
3. added console command for ring effect suppression algoritm on/off
4. updated audiocodec driver - added AGC setup
5. added UI board IC tests and a command to test
6. added EEPROM IC writing time tests and a command to test

30.12.2021
Beta version of software for intercom consoles (PDO), stage 1+, patch 1
1. updated codes of devices and their processing for exchange with the configurator, according to technical requirements
2. updated codes of buttons functions, according to technical requirements
3. added commands for changing and printing parameters of the sound ring effect suppression algorithm
4. updated algorithm for ring effect suppression (avoiding periodic appearance of the ring effect during one-way conversation in duplex mode)

16.12.2021
Beta version of software for intercom consoles (PDO), patch 3
1. updated project file for building from command line.
2. updated EEPROM test result message output.
3. updated connection manager - added checks for receiving packets from non-existent subscribers.