     [..]
     The ETH HAL driver can be used as follows:

      (#)Declare a ETH_HandleTypeDef handle structure, for example:
        ETH_HandleTypeDef heth; ETH_HandleTypeDef heth; (ethernetif.c)

      (#)Fill parameters of Init structure in heth handle

      (#)Call HAL_ETH_Init() API to initialize the Ethernet peripheral (MAC, DMA, …)
hal_eth_init_status = HAL_ETH_Init(&heth);(ethernetif.c) - OK

      (#)Initialize the ETH low level resources through the HAL_ETH_MspInit() API:
        (##) Enable the Ethernet interface clock using
        (+++) __HAL_RCC_ETH1MAC_CLK_ENABLE()
        (+++) __HAL_RCC_ETH1TX_CLK_ENABLE()
        (+++) __HAL_RCC_ETH1RX_CLK_ENABLE()

        (##) Initialize the related GPIO clocks
        (##) Configure Ethernet pinout
        (##) Configure Ethernet NVIC interrupt (in Interrupt mode)

      (#) Ethernet data reception is asynchronous, so call the following API
        to start the listening mode:
        (##) HAL_ETH_Start():
        This API starts the MAC and DMA transmission and reception process,
        without enabling end of transfer interrupts, in this mode user
        has to poll for data availability by calling HAL_ETH_IsRxDataAvailable()
        (##) HAL_ETH_Start_IT():
        This API starts the MAC and DMA transmission and reception process,
        end of transfer interrupts are enabled in this mode,
        HAL_ETH_RxCpltCallback() will be executed when an Ethernet packet is received

      (#) When data is received (HAL_ETH_IsRxDataAvailable() returns 1 or Rx interrupt
        occurred), user can call the following APIs to get received data:
        (##) HAL_ETH_GetRxDataBuffer(): Get buffer address of received frame
        (##) HAL_ETH_GetRxDataLength(): Get received frame length
        (##) HAL_ETH_GetRxDataInfo(): Get received frame additional info,
        please refer to ETH_RxPacketInfo typedef structure

      (#) For transmission path, two APIs are available:
        (##) HAL_ETH_Transmit(): Transmit an ETH frame in blocking mode
        (##) HAL_ETH_Transmit_IT(): Transmit an ETH frame in interrupt mode,
        HAL_ETH_TxCpltCallback() will be executed when end of transfer occur

      (#) Communication with an external PHY device:
        (##) HAL_ETH_ReadPHYRegister(): Read a register from an external PHY
        (##) HAL_ETH_WritePHYRegister(): Write data to an external RHY register

      (#) Configure the Ethernet MAC after ETH peripheral initialization
        (##) HAL_ETH_GetMACConfig(): Get MAC actual configuration into ETH_MACConfigTypeDef
        (##) HAL_ETH_SetMACConfig(): Set MAC configuration based on ETH_MACConfigTypeDef

      (#) Configure the Ethernet DMA after ETH peripheral initialization
        (##) HAL_ETH_GetDMAConfig(): Get DMA actual configuration into ETH_DMAConfigTypeDef
        (##) HAL_ETH_SetDMAConfig(): Set DMA configuration based on ETH_DMAConfigTypeDef

      -@- The PTP protocol offload APIs are not supported in this driver.

  *** Callback registration ***
  =============================================

  The compilation define USE_HAL_ETH_REGISTER_CALLBACKS when set to 1
  allows the user to configure dynamically the driver callbacks.
  Use Function @ref HAL_ETH_RegisterCallback() to register an interrupt callback.

  Function @ref HAL_ETH_RegisterCallback() allows to register following callbacks:
    (+) TxCpltCallback : Tx Complete Callback.
    (+) RxCpltCallback : Rx Complete Callback.
    (+) DMAErrorCallback : DMA Error Callback.
    (+) MACErrorCallback : MAC Error Callback.
    (+) PMTCallback : Power Management Callback
    (+) EEECallback : EEE Callback.
    (+) WakeUpCallback : Wake UP Callback
    (+) MspInitCallback : MspInit Callback.
    (+) MspDeInitCallback: MspDeInit Callback.

  This function takes as parameters the HAL peripheral handle, the Callback ID
  and a pointer to the user callback function.

  Use function @ref HAL_ETH_UnRegisterCallback() to reset a callback to the default
  weak function.
  @ref HAL_ETH_UnRegisterCallback takes as parameters the HAL peripheral handle,
  and the Callback ID.
  This function allows to reset following callbacks:
    (+) TxCpltCallback : Tx Complete Callback.
    (+) RxCpltCallback : Rx Complete Callback.
    (+) DMAErrorCallback : DMA Error Callback.
    (+) MACErrorCallback : MAC Error Callback.
    (+) PMTCallback : Power Management Callback
    (+) EEECallback : EEE Callback.
    (+) WakeUpCallback : Wake UP Callback
    (+) MspInitCallback : MspInit Callback.
    (+) MspDeInitCallback: MspDeInit Callback.

  By default, after the HAL_ETH_Init and when the state is HAL_ETH_STATE_RESET
  all callbacks are set to the corresponding weak functions:
  examples @ref HAL_ETH_TxCpltCallback(), @ref HAL_ETH_RxCpltCallback().
  Exception done for MspInit and MspDeInit functions that are
  reset to the legacy weak function in the HAL_ETH_Init/ @ref HAL_ETH_DeInit only when
  these callbacks are null (not registered beforehand).
  if not, MspInit or MspDeInit are not null, the HAL_ETH_Init/ @ref HAL_ETH_DeInit
  keep and use the user MspInit/MspDeInit callbacks (registered beforehand)

  Callbacks can be registered/unregistered in HAL_ETH_STATE_READY state only.
  Exception done MspInit/MspDeInit that can be registered/unregistered
  in HAL_ETH_STATE_READY or HAL_ETH_STATE_RESET state,
  thus registered (user) MspInit/DeInit callbacks can be used during the Init/DeInit.
  In that case first register the MspInit/MspDeInit user callbacks
  using @ref HAL_ETH_RegisterCallback() before calling @ref HAL_ETH_DeInit
  or HAL_ETH_Init function.

  When The compilation define USE_HAL_ETH_REGISTER_CALLBACKS is set to 0 or
  not defined, the callback registration feature is not available and all callbacks
  are set to the corresponding weak functions.